## Slide 1: RAMP Code Consolidation
Caitlin Condon
Julia Flaherty
PNNL-SA-179075
October 27th, 2022
Pacific Northwest National Laboratory

## Slide 2: Outline
History and Motivation for RAMP Code Consolidation
RAMP Code Consolidation (SIERRA)
Atmospheric Engine Code Consolidation Efforts
Next Steps

## Slide 3: RAMP Codes

## Slide 4: NRC Need
NRC Non-Light Water Reactor (Non-LWR) Vision and Strategy, Volume 4 –– Licensing and Siting Dose Assessment Codes (RAMP)
  describes the computer codes in RAMP and how they would be applied to each of the principal non-LWR design types, and summarizes the tasks necessary to resolve “gaps” in the capability to model and simulate those designs with the accuracy required by the regulator
Code consolidation can help resolve the identified gaps in the RAMP suite of codes

## Slide 5: Code Functions and Data Flow
R
Source Term
What radionuclides to consider for potential release to the environment?
Release Conditions
How they are released, e.g., chemistry, particle size, buoyancy, building size, stack height?
Environmental Consequences
What is the dose?
Environmental Dispersion
Where does it go…how much, how far, how fast?
Report Out
Data
Source Term Data
Releases
Met
Data
Environmental Fate
RAMP Codes
Input to RAMP Codes

## Slide 6: Legacy Issues Facing RAMP Codes
Incompatible with non-LWRs
Ownership issues
Lack of standardized code development
Lack of maintenance
Dated science
Lack of standardized quality assurances
Functional redundancy/data transfer
Inefficiency

## Slide 7: What is the broader challenge?
Prepare for Non-LWRs
Modernize
Consolidate

## Slide 8: Options Paper for RAMP Code Modernization and Consolidation
The computer codes in the RAMP program have been developed since the 1970’s to address specific regulatory needs.
These codes today have numerous current and legacy issues that reduce the efficiency of operation and maintenance of the codes and increase cost. In their current state, these codes are also unable to fully assess radiological doses from advanced non-light water reactor designs.
These current and legacy issues could be addressed by transforming the current suite of single-purpose radiation protection and dose assessment computer codes to a consolidated functional and modern suite of codes that is modular, flexible, efficient and user-friendly.
Thesis Statement

## Slide 9
RAMP Codes Consolidation and Modernization
Three Concept “Pillars:”
Consolidate Current Code Capabilities functional “Engines”
Develop Standardized Data Transfer Schema
Build a Single and Separate User Interface (UI)

## Slide 10
Consolidated Engines would perform calculations for dispersion and consequence analysis:
  Dispersion
  Accumulation
  Exposure
  Consequence
Pillar 1: Proposed Functional “Engines” will standardize input/output

## Slide 11: Overlapping Capabilities in Current RAMP Codes

## Slide 12: Code Functional Capability Examples
Atmospheric Dispersion
Biota Exposure
Environmental Accumulation
River/Lake Dispersion
Dose Coefficients
Dosimetry
Human Exposure
PAVAN

## Slide 13: Code Functional Capability Examples
Atmospheric Dispersion
Biota Exposure
Environmental Accumulation
River/Lake Dispersion
Dose Coefficients
Dosimetry
Human Exposure
GENII Biota

## Slide 14: Code Functional Capability Examples
Atmospheric Dispersion
Biota Exposure
Environmental Accumulation
River/Lake Dispersion
Dose Coefficients
Dosimetry
Human Exposure
GASPAR II

## Slide 15: Pillar 2: Develop Standardized Data Transfer Schema
JSON Input
JSON Output

## Slide 16: Pillar 2: Develop Standardized Data Transfer Schema
A JSON schema for the RAMP suite of codes will be
  Flexible
    Will allow additions of new variables yet unknown for advanced reactor designs
    Variable data will not need to appear in the data transfer file in a particle order, will only need to be in the json format and have the associated keyword
  Standardized
    All data transfer into the code, between functional engines, and out to the user will be in the same standard format
  Modern
    Widely used format

## Slide 17: Pillar 3: A Single Modern Use Interface
Improved UI will provide a modern user experience
User interface will be separate from the functional engines
  Updating or changing the user interface will not inadvertently affect the quality of the functional capabilities
  Allows for the possibility of developing a web-based user experience or mobile application
User interface will require updates and maintenance
  Will only have one user interface to maintain

## Slide 18: What are the Benefits of the Approach?
Accommodates anticipated needs for non-LWR Designs
Modernizes code languages and user experience
Reduces number of codes to upgrade and maintain
Standardizes Inputs and Outputs
Flexible design for future expansion or updates

## Slide 20: Code Consolidation Methodology
Establishing requirements in a “Requirements Document”
Establishing quality assurance protocols
  A software Quality Assurance Plan (SQAP) was established for the entire development project
Flexibility and anticipation of growth and change

## Slide 21: SIERRA User Interface Development
SIERRA provides a user interface which can be used to define the type of simulation that is to be run
Using a defined directory structure, SIERRA controls the execution and data transport of modules during a simulation
Modules are independent applications and are not directly integrated into the SIERRA application
Modules are considered “Black Box” and are executed as synchronous child processes by the SIERRA application
While SIERRA was developed using the C# programming language, modules can be developed using any programming language that produces an executable file
Module executables are required to accept input and output paths as command line arguments
Modules provide their own interfaces and post processing functionality
SIERRA is intended to allow for the addition of modules without requiring code changes to UI

## Slide 22: Atmospheric Dispersion Module Development
Julia Flaherty, PNNL

## Slide 23: Current Efforts in Code Consolidation
Prototype Development
  Atmospheric Dispersion Module
    JSON Schema for variables of interest
  Functional User Interface
Testing Activities
  Usability testing of the User Interface
  Functional testing of code
    Verify data transfer
    Evaluate code accuracy and consistency with ARCON, PAVAN, and XOQDOQ results
Quality Assurance (QA)
  Software QA Plan defines QA approach to provide adequate confidence that
    Software development process is controlled
    Software products meet established requirements

## Slide 24: Agile Software Development

## Slide 25
Prototype Development: Consolidating Current Atmospheric Dispersion Codes
Code | Description
ARCON | Used to calculate relative air concentrations (/Qs) in support of control room habitability assessments required by general design criteria (GDC) 19 of 10 CFR Part 50 Appendix A and RG 1.194.
PAVAN | Used to estimate relative ground-level air concentrations (/Q s) resulting from radioactive material releases from design-basis accidents at NPPs following the methodology in RG 1.145.
NRCDose | Software suite that integrates the functionality of three individual Fortran codes: LADTAP II, GASPAR II, and XOQDOQ, which were developed by the NRC and have been in use by NPP licensees and the NRC staff for assessments of liquid radioactive releases and offsite doses, gaseous radioactive effluents and offsite doses, and meteorological transport and dispersion, respectively. XOQDOQ implements the atmospheric dispersion modeling described in RG 1.111.
Near Field: ~100s of meters
Mid-Field: ~10 km
Far Field: Up to ~80 km

## Slide 26: Atmospheric Dispersion Engine Working Prototype
Functional Engine within the larger Consolidated Engine Framework

## Slide 27: SIERRA Prototype Overview
Regulatory vs Research
Analysis Types:
  Control Room Analysis
  Design Basis Accidents
  Routine Analysis
Module Selection:
  Atmospheric Dispersion

## Slide 28: Common Input Needs / User Interface Panels
Source
Receptor (Control Room, Routine Analysis)
Terrain (Design Basis, Routine Analysis)
Meteorology
  All models use hourly data per RG1.23
Output
Notes:   Met panel: Control Room Habitability includes roughness length; DBA, Routine Analysis omits roughness length

## Slide 29: Control Room Habitability Assessment (ARCON)
1900 m2
Building Area
10 m
Release Height
15 m
Intake Height
45 m
Receptor Distance
Direction to Source
230 degrees
Source
Receptors
Meteorology
Output

## Slide 30: Design Basis Analysis (PAVAN)
Source
Terrain
Meteorology
Output

## Slide 31: Routine Analysis (XOQDOQ)
45 m
Release Height
980 m
distance
2850 m
distance
Site boundary distance
715 m
Source
Receptors
Terrain
Meteorology
Output

## Slide 32: Example Output Panel Routine Analysis
Two areas in the panel:
  Output Files
  Output Viewer

## Slide 33: Next Steps
In Progress:
SIERRA User Interface
Atmospheric Dispersion Module
Source Term Module
Upcoming:
River/Lake Dispersion Module
Environmental Accumulation
Human Exposure
Dose Coefficients
Dose/Consequences
Non-Human Biota exposure