## Slide 1: Regulatory Considerations of Non-LWR Source Terms
Michelle Hart
U.S. Nuclear Regulatory Commission
November 3, 2022
Notes: About the Image: A Glass From the Past
While taking a closer look at ancient glass to better understand how it changed over time, Pacific Northwest National Laboratory scientists made an unexpected discovery-the remains of bacteria that once lived on the surface. PNNL researchers and collaborators are delving into the past to further their knowledge about the stability of glass that will be used to safely store low-activity nuclear waste at the Hanford Site. With support from the Department of Energy's Office of Environmental Management, International Programs through the Office of River Protection, they are analyzing this glass found in Swedish hillforts that predates the Vikings because it has a chemical composition similar to what will be produced at Hanford's Waste Treatment and Vitrification Plant and has been "stored" in a known environment for more than 1,500 years.
Research team: David Peeler, Bruce W. Arey, Carolyn I. Pearce, Tamas Varga, Micah D. Miller, Michele Conroy and Michael J. Schweiger (all of PNNL); John S. McCloy (Washington State University); Jamie L. Weaver (National Institute of Standards and Technology); Edward Vicenzi and Thomas Lam (Smithsonian Institution's Museum Conservation Institute); Rolf Sjoblom (Tekedo AB); Eva Hjarthner-Holdar and Erik Ogenhall (Arkeologerna); and Albert A. Kruger (Department of Energy Office of River Protection). The image was colorized by Nathan Johnson (PNNL).
Instrument: Scanning electron microscope and focus ion beam hybrid
https://www.flickr.com/photos/pnnl/24220123368/in/photolist-fqwiqF-aBF44N-fqwj9R-aEuQHd-CUfsRW-pZVLNL-aPjNkZ-fxBosi-aErWsK-aBCnZk-ECMqka-aEr4hT-6yL625-6xvZrp-6xh38v-6xmeiY-VNqjUa-CJUXKp-CPUyAo-25kubq5-BUPMLB-211nysv-Chikdn-Cq6fRm-BscBWe-CnhkRJ-CiHawx-CPUwEu-BUGK7J-CiHawn-BUPKMg-CGEBLY-BUGHTw-CJV1jx-CPUxnw-CSdgpF-CSdj4D-CJUWi6-CPUwFm-BXsubh-CPUxJd-CiHdVB-BUGG5b-BUGHYm-22DixCm-243ex8R-Cq6jHQ-CGEzzy-PEd3HJ-P9S5sd

## Slide 2: Reactor accident consequence analysis
Siting and safety analysis for reactor licensing
Control room habitability design criterion
Environmental consequences of accidents
  Environmental impact statement for compliance with the National Environmental Policy Act (NEPA)
Regulatory and cost-benefit analyses

## Slide 3: Accident consequence analysis: Newer uses for advanced reactors
Probabilistic risk assessment (PRA)
  Non-LWR PRA standard does not use risk surrogates like core damage frequency
Risk-informed, performance-based methodology for non-LWR licensing basis development, a.k.a. Licensing Modernization Project (LMP)
  RG 1.233 endorses NEI 18-04 approach to selecting licensing basis events, classifying structures systems and components and special treatment, and assessing defense-in-depth
Plume exposure pathway emergency planning zone size determination
Alternative security requirements – ongoing rulemaking
10 CFR Part 53 risk-informed, technology-inclusive regulatory framework for advanced reactors – ongoing rulemaking

## Slide 4: Accident source terms for new LWR designs
RG 1.183 provides source term models and assumptions that are acceptable to the NRC for BWRs and PWRs
  Developed for large LWRs like the currently operating commercial power reactors
  Deterministic
  Accident-specific guidance for LWR design basis accidents with damage to irradiated fuel
  Guidance on dose calculation methodology
For LWR designs that are very different than the current reactors, some models and assumptions in RG 1.183 may not be applicable or need justification for use
Some accident analyses described in the RG may not apply
  e.g., PWR locked rotor accident would not apply to a natural circulation plant that does not have reactor coolant pumps

## Slide 5: Non-LWR accident source terms
Non-LWR designs may use mechanistic source terms
Plant-specific identification of events/accidents and development of accident source terms
  Some may choose to provide a postulated maximum hypothetical accident (MHA) and deterministic source term, similar to non-power reactor licensees
No RGs with specific guidance on development of mechanistic source terms or pre-accepted source terms for non-LWR technologies
  RG 1.183, regulatory position C.2, “Attributes of an Acceptable AST,” may be useful
  SECY-93-092 included staff recommendations on non-LWR source terms

## Slide 6: Mechanistic source term
SECY-93-092 described a mechanistic source term (MST) as
  …the result of an analysis of fission product release based on the amount of cladding damage, fuel damage, and core damage resulting from the specific accident sequences being evaluated. It is developed using best-estimate phenomenological models of the transport of the fission products from the fuel through the reactor coolant system, through all holdup volumes and barriers, taking into account mitigation features, and finally, into the environs.

## Slide 7: SECY-93-092 provisions for Staff assurance re: MST development
  The performance of the reactor and fuel under normal and off-normal conditions is sufficiently well understood to permit a mechanistic analysis. Sufficient data should exist on the reactor and fuel performance through the research, development, and testing programs to provide adequate confidence in the mechanistic approach.
  The transport of fission products can be adequately modeled for all barriers and pathways to the environs, including the specific consideration of containment design. The calculations should be as realistic as possible so that the values and limitations of any mechanism or barrier are not obscured.
  The events considered in the analyses to develop the set of source terms for each design are selected to bound severe accidents and design-dependent uncertainties.
  The design-specific source terms for each accident category would constitute one component for evaluating the acceptability of the design.

## Slide 8: Accident source term development considerations
Event selection, scenarios
Balance of prevention vs. mitigation
Relationship to functional containment
  A barrier, or set of barriers taken together, that effectively limit the physical transport of radioactive material to the environment (SECY-18-0096)
Relationship to PRA
Adequacy of modeling and simulation tools
Understanding of fission product transport phenomena
Uncertainty

## Slide 9: Source Term Information Webpage
https://www.nrc.gov/reactors/new-reactors/advanced/nuclear-power-reactor-source-term.html
One-stop shop for reactor accident source term information
Publicly available

## Slide 10: Source Term Information Webpage
Links:
History and evolution of LWR source term
NRC analytical tools and past studies
Advanced reactor source term demonstration
  Full-plant models for several representative non-LWR designs
  Demonstrates use of SCALE and MELCOR codes
Source term approaches
Information on developing non-LWR source terms (what to do)
Reports on reactor source term
Presentations on non-LWR source term
https://www.nrc.gov/reactors/new-reactors/advanced/nuclear-power-reactor-source-term.html
Discussion of accident source terms
Linked list of documents relevant to development of non-LWR accident source terms for licensing