## Slide 1: CAUG 10: Tallies
Charlotte Rose MS (RHP)

## Slide 2: Last Class
Sources

## Slide 3: Intermediate MCNP
Trey will share his experience with MCNP
Tallies

## Slide 4: Tallies
At the heart of our work
Accounting of activities
What the statistics are reported on; statistics are not a report of the problem or model as a whole
Remember from first class: we cannot recover lost info! (be careful of areas with zero importance, and tally where you want to without ignoring other areas you think won’t sample)
7 types

## Slide 6: Tallies
Note: no particle designator!
Or use with dose functions

## Slide 7: Ways to tally Dose
PIMAL Phantom
ICRU Sphere
  Sphere 30 cm diameter (15 cm radius)
  ~ 14 L
ICRU Slab
  30 cm x 30 cm x 15 cm
  ~14 L
ICRU 4-component tissue

## Slide 8: Ways to tally Dose
F4n Tally with dose function
F6n Tally *need* multipliers for biological dose
  Most exact
  F4 Tally with FM -1 -4 (total collision heating)
+F6 Energy from all particles averaged over the cell
*F8n energy deposition
  Always P and E (particle designation does not matter, all photons and electrons are tracked
  Results not per g

## Slide 13: Tallies
Normalized to one
Activity can be input in the WGT parameter (SDEF card) or modified after

## Slide 14: Tally Energy
Default to one energy bin with total energy
E0 will set up energy bin structure for all tallies in model
Entered in order of increasing magnitude
  If energy of a particle exceeds highest bin, it will NOT BE TALLIED
  eg: E4 0.01 0.1 1 10
    This will break down the tally into 4 energy bins:
      from 0 to 0.01
      from 0.01 to 0.1
      from 0.1 to 1
      from 1 to 10