## Slide 1: Extravasation FLOW AND DOSIMETRY MODEL UPDATE October 26, 2023
RENAISSANCE CODE DEVELOPMENT
Roland Benke, PhD, CHP

## Slide 2: outline
Objective | Overview | Project Scope
Model Descriptions
Summary

## Slide 3: OBJECTIVE
Build a computational tool (software) to calculate 3D dose distributions in tissue with interfaces and flexibility appropriate for radionuclide extravasations
Extravasation occurs when the radiopharmaceutical intended for the bloodstream leaks into surrounding tissue.

## Slide 4: What MATTERS?
Physical and chemical characteristics of the radiopharmaceutical
Administration flow rate and duration (gravity method, infusion pump, injection)
Biological composition and structure at the site of extravasation (tissue matrix)
Physical changes to the site (elevation of site, warm compress)
Biophysical movement and dissipation of extravasated fluid (flow & vascular removal)
  Volume of tissue affected by extravasated fluid
  Extravasated fluid concentrations in tissue over time
Radioactivity extravasated (initial source term)
Radioactive decay, emission type and energy

## Slide 5: PRoject SCOPE
Insights & Action
This presentation
Software
Model
Graphical user interface
Software coding
Output visualization
Model development
Documentation
Users

## Slide 6: What IS BEING CALCULATED?
Movement of radioactive extravasated fluid in tissue
Activity concentration in tissue over time in three dimensions
Local tissue dose over time in three dimensions
Activity Concentration Model
Flow Model
Dosimetry Model

## Slide 7
Flow Model

## Slide 8: FLEXIBLE LAYERING for extravasation modeling
to accommodate a variety of circumstances
  Deep infiltration without appreciable extravasation in epidermis
  Dermal extravasation with explicit infiltration into the epidermis
  Confined extravasation within multiple dermal layers
(a) (b) (c)
Kwak and Chang (2020) Compression of the lateral antebrachial cutaneous nerve due to leakage of iron after an intravenous iron infusion. Diagnostics 2020, 10, 516. Figure 1(C).

## Slide 9: HOMOGENEOUS TISSUE MATRIX
before extravasation
Interstitial components include fine vascular bathed in extracellular fluid
after extravasation
In initial modeling
Fluid movement is tracked without tissue shape changes
Stationary grid

## Slide 10
Two layers shown {Dermis, Hypodermis}
Vascular removal rates v change over time {Statis, Degraded, Normal}

## Slide 11: FLOW PRIMARILY DRIVEN BY PRESSURE
STAGE 1
External driving force to flow
Theis equation for confined flow
2D lateral calculation initially
+ vertical fluid distribution
STAGE 2
No external driving force
Darcy flow with hydrostatic pressure from fluid in tissue
3D calculation

## Slide 12: CONFINED FLOW IN STAGE 1

## Slide 13: THEIS EQUATION USED IN STAGE 1
Exponential integral definitions
Hydrostatic pressure head [cm] as function of space and time

## Slide 14: darcy flow AND TRANSMISSIVITY
Darcy flow velocity [cm s-1] depends on pressure differentials and properties of the flow matrix
“Effective” accounts for spatial heterogeneity within the tissue matrix

## Slide 15: EFFECTIVE TRANSMISSIVITY FOR TISSUE LAYERS
Calculated as a weighted sum of transmissivities for individual layers i

## Slide 16: LATERAL Extravasated FLUID FLOW DURING ADMINISTRATION
For a constant volumetric flow rate of the radiopharmaceutical during administration
Quasi-steady-state conditions for lateral extravasation flow would be reached within ~5 minutes
Simplification is made to remove the time dependence from the Theis equation
Radial pressure gradient from the Theis equation yields a quasi-steady-state velocity profile:
Bonta et al. (2011) Extravasation of a therapeutic dose of 131I-metaiodobenzylguanidine: Prevention, Dosimetry, and Mitigation. J Nucl Med 52: 1418-1422.

## Slide 17: Extravasated FLUID APPORTIONED TO LAYERS BASED ON TRANSMISSIVITY
for radial rings
for tissue layers
Tissue volume [cm3] for layer i within radial ring j
Volume of extravasated fluid [ml] in radial ring j is apportioned to layer i

## Slide 18
STAGE 1 FLOW TESTiNg EXAMPLE

## Slide 19
after 15 s
Extravasated fluid volume concentration [ml cm-3]
TEST OF LARGE-VOLUME EXTRAVASATION IN TISSUE DURING ADMINSTRATION
Top layer (0.2 cm)
Middle layer (0.3 cm)
Bottom layer (0.5 cm)

## Slide 20
after 1 min
TEST OF LARGE-VOLUME EXTRAVASATION IN TISSUE DURING ADMINSTRATION
Extravasated fluid volume concentration [ml cm-3]
Top layer (0.2 cm)
Middle layer (0.3 cm)
Bottom layer (0.5 cm)

## Slide 21
after 3 min
TEST OF LARGE-VOLUME EXTRAVASATION IN TISSUE DURING ADMINSTRATION
Extravasated fluid volume concentration [ml cm-3]
Top layer (0.2 cm)
Middle layer (0.3 cm)
Bottom layer (0.5 cm)

## Slide 22
after 10 min
TEST OF LARGE-VOLUME EXTRAVASATION IN TISSUE DURING ADMINSTRATION
Extravasated fluid volume concentration [ml cm-3]
Top layer (0.2 cm)
Middle layer (0.3 cm)
Bottom layer (0.5 cm)

## Slide 23
after 20 min
TEST OF LARGE-VOLUME EXTRAVASATION IN TISSUE DURING ADMINSTRATION
Extravasated fluid volume concentration [ml cm-3]
Top layer (0.2 cm)
Middle layer (0.3 cm)
Bottom layer (0.5 cm)

## Slide 24
after 40 min
TEST OF LARGE-VOLUME EXTRAVASATION IN TISSUE DURING ADMINSTRATION
Extravasated fluid volume concentration [ml cm-3]
Top layer (0.2 cm)
Middle layer (0.3 cm)
Bottom layer (0.5 cm)

## Slide 25
after 60 min
TEST OF LARGE-VOLUME EXTRAVASATION IN TISSUE DURING ADMINSTRATION
Extravasated fluid volume concentration [ml cm-3]
Top layer (0.2 cm)
Middle layer (0.3 cm)
Bottom layer (0.5 cm)

## Slide 26: STAGE 2 AFTER ADMINISTRATION CEASES
Residual pressure from extravasated fluid temporarily trapped in tissue

## Slide 27: STAGE 2 LATERAL FLOW in 3D GRID

## Slide 28: STAGE 2 Vertical FLOW in 3D GRID

## Slide 29: VASCULAR REMOVAL of extravasated FLUID

## Slide 30: RELATIVE ELEVATION HEAD
Fig. 3(C) in Iori et al. (2022)
https://doi.org/10.21203/rs.3.rs-2009242/v1

## Slide 31: RADIAL DISTANCES FOR ELEVATION HEAD

## Slide 32
STAGE 2 FLOW TESTiNg EXAMPLE

## Slide 33
TEST OF LARGE-VOLUME EXTRAVASATION FLOW AFTER ADMINSTRATION
Top layer (0.2 cm)
Middle layer (0.3 cm)
Bottom layer (0.5 cm)
Extravasated fluid volume conc. [ml cm-3]
Affected tissue is immediately elevated
when administration ceases + 0 min

## Slide 34
TEST OF LARGE-VOLUME EXTRAVASATION FLOW AFTER ADMINSTRATION
Top layer (0.2 cm)
Middle layer (0.3 cm)
Bottom layer (0.5 cm)
Extravasated fluid volume conc. [ml cm-3]
Affected tissue is immediately elevated
when administration ceases + 18 min

## Slide 35
TEST OF LARGE-VOLUME EXTRAVASATION FLOW AFTER ADMINSTRATION
Top layer (0.2 cm)
Middle layer (0.3 cm)
Bottom layer (0.5 cm)
Extravasated fluid volume conc. [ml cm-3]
Affected tissue is immediately elevated
when administration ceases + 33 min

## Slide 36
TEST OF LARGE-VOLUME EXTRAVASATION FLOW AFTER ADMINSTRATION
Top layer (0.2 cm)
Middle layer (0.3 cm)
Bottom layer (0.5 cm)
Extravasated fluid volume conc. [ml cm-3]
Affected tissue is immediately elevated
when administration ceases + 46 min
Lower maximum
in this scale
Lower maximum
in this scale

## Slide 37
TEST OF LARGE-VOLUME EXTRAVASATION FLOW AFTER ADMINSTRATION
Top layer (0.2 cm)
Middle layer (0.3 cm)
Bottom layer (0.5 cm)
Extravasated fluid volume conc. [ml cm-3]
Affected tissue is immediately elevated
when administration ceases + 54 min
Lower maximum
in this scale
Lower maximum
in this scale

## Slide 38
TEST OF LARGE-VOLUME EXTRAVASATION FLOW AFTER ADMINSTRATION
Top layer (0.2 cm)
Middle layer (0.3 cm)
Bottom layer (0.5 cm)
Extravasated fluid volume conc. [ml cm-3]
Affected tissue is immediately elevated
when administration ceases + 58 min
Lower maximum
in this scale
Lower maximum
in this scale

## Slide 39
Activity Concentration Model

## Slide 40: ACTIVITY CONCENTRATION MODEL
Converts extravasated fluid in tissue into activity per unit volume
Applies to 3D computational grid of tissue with unit density that does not flex or deform
Two input parameters
Model without F input & model with F input
Transfers spatial- and time-dependent concentration data to the dosimetry model
Includes time-integrated activity concentration
Activity concentration in tissue ≤ Activity concentration of administered radiopharmaceutical

## Slide 41: ACTIVITY CONCENTRATION in tissue without F INPUT
For cubic computational cells, A = s2 lateral area [cm2]

## Slide 42: ACTIVITY CONCENTRATION WHEN F INPUT is provided

## Slide 43
Dosimetry Model

## Slide 44: PHOTON DOSE RATE
Point kernel for uncollided photons (no scatter) with cell center to cell center distance r
Point-pair distribution for 26 target cells immediately surrounding source cell

## Slide 45: PHOTON DOSE RATE FROM Point-pair distribution
Source cell S
Target cell T

## Slide 46: Alpha particle DOSE RATE
To source cell (self-irradiation)
To adjacent cells sharing a planar face

## Slide 47: ELECTRON DOSE RATE
Based on SkinDose in VARSKIN+ 1.0 computer code
Details in NUREG/CR-6918, Revision 4 (July 2021)
Scaled absorbed dose distribution

## Slide 48: SUMMARY
Local Tissue Dose from Extravasation
Flow Model
  Stage 1 during Radiopharmaceutical Administration
  Stage 2 after Radiopharmaceutical Administration
Activity Concentration Model
Dosimetry Model
Benjegerdes et al. (2017) Focal cutaneous squamous cell carcinoma following Radium-223 extravasation. Baylor University Medical Center Proceedings 30:1, 78-79, DOI: 10.1080/08998280.2017.11929538.